## Slide 1
Revise parameter classification
Classify controls by their effect on data, constraints, and decision structure.
TYPE
CURRENT OPERATIONS
EFFECT ON THE OPTIMIZATION MODEL
Input values
scenario
scale_pq_load — PQ_1 +10%
set_line_rate — Line_1 rate_a = 0.9
Updates demand or line limits. Existing variables, objective terms, and constraint definitions remain; changed limits may still alter the feasible region.
Device / topology status
scenario
set_line_status — open Line_1
set_generator_status — disable unit
Changes device availability, network state, and solve inputs. Results can shift without adding a decision-variable class.
Routine settings
scenario
set_config_t — ED interval = 0.5 h
Changes the active routine’s time setting and rebuilds its model; adds no custom objective term or constraint.
Existing constraint toggles
formulation
set_constraint_status — disable plfub
set_ramping_status — disable ED ramping
Changes which existing constraints participate in the solve. This is a formulation change; no new constraint is defined.
Add objective / constraint
formulation
add_dispatch_cost
set_total_generation_cap
First use adds an objective term or generation-cap constraint. Repeated use updates its coefficient or upper limit.
New variables + model rewrite
formulation
replace_generator_with_ibr
DCOPF adds pibr / pcurt, availability limits, and cost terms, then rewrites nodal power balance (active-power scope).
Sources: formulation_controls.json:43–179 · parameter_controls.py:230–302 · formulation_edit.py:105–129
Monthly Meeting · 10/26/2026
4